## Slide 1: VentTube

## Slide 2: Good Natural Ventilation Principles
Inlet
Inlet
Exhaust
Cross Winds
Every building is different =
Every building ventilates differently
i) Maximise Inlet and Exhaust
ii) Inlet (x2-4) to Exhaust Area
Increased Stocking rate = more heat/m3

## Slide 3: Side Inlets
(Automatic) Curtain Sided
Open Sided
Spaced Board /
Vent Cladding
Adjoined Buildings

## Slide 4: Exhaust / Ridge
Ventilating Light Ridge
Open Ridge
Vent. Cranked Ridge

## Slide 5
Plan View
End View
Prevailing wind passes perpendicular to ridge
Air passes through open sides
Air accelerates over the ridge, causing suction
= Good Natural
Ventilation
Prevailing wind aligns with ridge
Air hits end of building (often not open)
Some air passes over ridge but not accelerated
= Reduced Natural
Ventilation
Plan View
Side View
Prevailing Wind
Building Orientation

## Slide 6: Mechanical Ventilation Options
VentTube Fresh
VentTube Cool
Cool - Chill effect
Fresh – Air replacement

## Slide 7: VentTube Fresh

## Slide 8: Calf Ventilation Common Issues
Calves are lower priority for housing
Calves are often housed with older animals, cross contamination of dirty air
Exposed to temperature fluctuations, calves very sensitive to temperature changes (LCT)
Difficulty producing ideal ventilation rate and low air speed throughout building with mechanical ventilation (fans)
Natural ventilation systems lack control to provide right microenvironment in the calf pen
Youngstock– Limited heat generation, limited stack effect, poor air exchanges

## Slide 9: Calf Ventilation Signs of Poor Ventilation
Smell within the building, is it damp? Smell of ammonia?
Cobwebs and dust build-up? Shows little ventilation and still air
Rust on roof purlins, fixings? Damp environment, moisture
Calves laying in certain areas, unevenly spread? Draughts?
Calves general behaviour or illness level?

## Slide 10: Ventilation and Calf Health
Bovine Respiratory Disease (BRD) is the leading cause of death in dairy and beef cattle; pneumonia is a component of BRD
Risk Factors associated with pneumonia in calves:
Low temperature
High humidity
Draught
Stress
Wet or minimal bedding
Stocking density
UK dairy sector

## Slide 11: Examples

## Slide 13: Calf Ventilation Aims for Existing Buildings
Improve aerial hygiene to limit respiratory disease
Provide controlled and consistent airflow
Remove moisture from the building
Remove excess heat and humidity from environment

## Slide 14: Calf Ventilation Minimum Requirements Reasons for requirements
Fresh Air
  Consistent clean, pathogen free air
  Ventilating building volume 4-8 times per hour (winter)
  Ventilating building volume 40-60 times per hour (summer)
Air speed
  Below 0.3m/s at 1.2m provide draught free environment during winter period
  1.3m/s at 1.2m during summer period
Exhaust opening
  0.04m2 minimum per calf (0.5 x the inlet m2)
Fresh Air
  Pathogens thrive in air with high moisture content
  Pathogens killed 10-20 times faster in fresh air
  Limits BRD and disease transmission
Air speed
  Prevents chilling of calf with lower immunity, hampers DWG
  Limits heat stress during hotter periods
Exhaust opening
  Allows dirty air to escape and continue airflow throughout the building

## Slide 15: VentTube Fresh Solution
Fresh air from outside the building
Bespoke design for the building and stock density.
System length 4.0 - 50.0 m
Stainless steel support wires at 12 o’clock position
Air speed is 0.25m/s at 1m above bedding
6-8 air changes per hour
Throw direction - hole positioning
Throw distance - static pressure and holes diameters
3 year guarantee

## Slide 16: VentTube Fresh
Holes spacing tailored to building layout
Building width dictates hole clock positions (3 or 4 per row)
Larger outer holes for greater throw distance
S35 Solid Grey material (lighter than previous material) – 350 gm2
Tubes now available from 20cm diameter
Robust welded assembly
Laser profiled holes

## Slide 17: VentTube Fresh
REFERENCE | QTY | PRODUCT DESCRIPTION
A1 | 1 | Fan
B1 | 1 | Fabric Tube
C1 | 2 | Mounting Bracket
D1 | 1 | M10 Turnbuckle
E1 | * | 65mm Quick Link
F1 | 1 | 4mm SS Wire Rope
G1 | * | 3mm SS Wire Rope and Loop
H1 | * | 3mm Wire Rope Grips
I1 | 8 | 5mm Wire Rope Grips
J1 | 2 | 6mm Wire Thimble
K1 | 1 | Jubilee Clip
L1 | 1 | Fan Cowling
M1 | 1 | Fan Mounting Sheet, Cladding only
N1 | 15 | 4.8x12mm SS Dome Rivets
O1 | * | Rope
P1 | * | Foam Tape (Panel Fan >Ø50cm)

## Slide 18: VentTube Fresh
VentTube Fresh check list

## Slide 19: VentTube Fresh

## Slide 20: VentTube Fresh Installation Examples

## Slide 21: VentTube Fresh Smoke Test

## Slide 22
VentTube Cool

## Slide 23
Impacts of Heat Stress
High Productivity Cows
Exhales 12-19 litre water per day
Produces 600-700 watts of heat /day
  And 330 g/CO2 / hour
  And 10 g/CH4 / hour
Thermocomfort zone 5-15 °C
Has no problems with cold (<-> people): thermoneutral zone -30°C

## Slide 24: VentTube Cool
THI Thermal Humidity Index

## Slide 25: Older Stock Ventilation Common Issues
Housed inside all year round
Re-use of general-purpose buildings
Additional buildings placed in close proximity
Buildings not orientated for prevailing winds to flow through the side
Buildings covered with cladding, boarding
Wide buildings hampering cross ventilation
Restricted airflow from surrounding area

## Slide 26: Older Stock Ventilation Signs of Poor Ventilation
Smell within the building, is it damp? Smell of ammonia?
Cobwebs and dust build-up? Shows little ventilation and still air
Rust on roof purlins, fixings? Damp environment, moisture
Cows bunching looking for high air speed?
Cows general behaviour/ health, signs of heat stress?

## Slide 27: Older Stock Ventilation Aims for Existing Buildings
Mature Animals – The Stack Effect works well, offering regular air exchanges
Provide high airflow for cooling
Remove excess heat and humidity from environment
Remove moisture produced by animals
Improve air quality with the building

## Slide 28: Older Stock Ventilation Minimum Requirements Reasons for requirements
Fresh Air
  Consistent clean, pathogen free air
  Ventilating building volume 60-90 times per hour (summer)
Air speed
  1.5-2.0m/s at 0.5m during summer period
Exhaust opening
  0.1m2 per adult stock (0.25-0.5 x the inlet m2)
Fresh Air
  Exchanges high moisture content for low, lowers humidity
  Lower humidity, high temperature can be before heat stress
Air speed
  Keep older stock cooler to reduce heat stress
Exhaust opening
  Allows dirty air to escape and continue airflow throughout the building

## Slide 29: Mechanical Ventilation Options
High-Volume Low-Speed
HVLS
Positive Pressure Tube Ventilation
PPTV
Standard Fans
High Speed
Directional
Recirculating internal air
Moving high air volumes
Multiple fans
Panel Fans
Galebreaker
VentTube® Cool
External Air Input (clean, less humid)
Air distributed directly over cubicle
Every cubicle has the same air delivery
One fan – more efficient

## Slide 30
Without VentTube® Cool
With VentTube® Cool

## Slide 31: VentTube Cool
Dairy cows require a relative in-barn temperature to be kept below 25°C
Heat stress has significantly negative impacts on factors such as milk yield, fertility and cell counts
VentTube Cool provides chill effect during hot periods to significantly improve cow wellbeing
The Galebreaker vision is to offer tube ventilation above every cow, in every barn, at every age.

## Slide 32: VentTube Cool
Fresh air drawn from outside – not recirculated
Mechanical retraction system to prevent damage from cross wind when not in-use
Airflow velocity target at optimum chill effect

## Slide 33
Galebreaker VentTube Cool
Product Introduction

## Slide 34
Galebreaker VentTube Cool
Advantages over traditional Fans

## Slide 35
Galebreaker VentTube Cool
Sales & Marketing Tools – Infographics
Tangible costs saving benefits + ROI
Figures adaptable to local markets
UK & EU average examples ready
Easy to translate
Social media engagement

## Slide 36
Galebreaker VentTube Cool
Product assembly – Installation
Key features
Ventilation fan
S35 fabric tube
Stainless support wire
Intake cowling
Vertical supports
Wall mounting plate

## Slide 37
Galebreaker VentTube Cool
Retraction system – Key features
Key features
Hand winch
Corner pulley
Pulley bracket
Lifting loops
Drop weight
Weight guide

## Slide 38
Galebreaker VentTube Cool
Retraction system – Video
Tube retraction system to store tube when not in use
Tube can be lifted to avoid damage when bedding sheds mechanically
Manual, low maintenance operation

## Slide 39
Galebreaker VentTube Cool
Site Checklist – Construction material for end fittings
Mounting fan into brick or block structure
What is the wall thickness? - can it support the fan weight
Is the wall load bearing- does the hole compromise the structural integrity – in an additional lintel required ?
Is there an internal cavity to fill
Cutting the hole using a core drill maybe possible
What fittings will be used (expanding bolts, chemical bolts?
Mounting fan into cladding structure
What is the cladding thickness – can it support the fan weight?
How is the cladding attached to the building – where are the cladding rails?
Is it is insulated cladding?
Is an additional structure require to support the fan? (particually with timber cladding)
Can the fan be bolted directly to the cladding?

## Slide 40
Galebreaker VentTube Cool
Site Checklist – Purlin suitably positioned for rope supports

## Slide 41
Galebreaker VentTube Cool
Site Checklist – Winch position

## Slide 42
Galebreaker VentTube Cool
Site Checklist – Counterweight position

## Slide 43
Galebreaker VentTube Cool
Site Checklist – Total cable length

## Slide 44
Galebreaker VentTube Cool
Site Checklist – Additional pulleys required

## Slide 45: VentTube Cool
Standard

## Slide 46: Standard Design
Optimal height 2.3 – 2.4m to bottom of tube
Air Speed: 2.0m/s @ 0.5m above bedding
Up to 50 m
Up to 40 m

## Slide 47: Standard Design – Building Measurements
Single Row
  A, B - Length of cubicles
Double Row
  C, D - Length of cubicles
  E - Width of passage way
3m
20m
15m

## Slide 48: VentTube Cool
Bespoke

## Slide 49
Galebreaker VentTube Cool
Sales & Marketing Tools – Site Survey Form
Key dimensions & specifications
Cross section & plan view sketches
Cubicle measurements

## Slide 50
Galebreaker VentTube Cool
Sales & Marketing Tools – Quotation Calculator

## Slide 51: VentTube Cool

## Slide 52
Galebreaker VentTube Cool
Sales & Marketing Tools – Brochure
New VentTube range brochure
Fresh + Cool
QR codes link to case studies
Available now
Real farm examples
  Challenges - VentTube solution
Template for regional versions
Social media postcards
Available via Dealerzone

## Slide 53: Marketing Support
VentTube Demonstration Frame
2.5 m x 2.4 m
Unique graphics for distributors
Part number for ordering:
MRKT-DIS-VT2425
Cost: €
Samples of S35 Grey material also available.

## Slide 54: THANK YOU FOR YOUR TIME ANY QUESTIONS?